## Slide 3
Webinar Notes
  Please use the Q & A utility to ask us any questions concerning
  the material being presented.
  Please contact Brittany Socha - chat line or email brittany.socha@arisafety.com if you would like a copy of the presentation.

## Slide 4
Leakage Current
Description
IEC 60601-1
IEC 60601-1 3rd Edition and the leakage current tests
Testing Examples
IEC 60601-1 discussion and reference diagrams
Network and MD
Tests called out for in the standard
Leakage testing video examples
Leakage Current Types
Touch Current
Patient Leakage
Patient Auxiliary Leakage
Mains on Applied Part Leakage
Touch Current Testing 102 – Learning Objectives

## Slide 5: Leakage Current Types
1 – IEC 60990 2nd edition: Methods of Measurement of Touch Current and Protective Conductor Current
2 – IEC 60601-1 3rd edition: Medical Electrical Equipment
Touch Current
Electric current through a human body when it touches one or more accessible parts of an installation or surface of electrical equipment1
Patient Leakage Current
Current flowing from the patient connections via the patient to earth
Also called Enclosure Leakage Current.
Patient Auxiliary Current
Mains on Applied Part
Current originating from the unintended appearance of a voltage from an external source on the patient and flowing from the patient via the patient connections of an F-Type applied part to earth.
Current flowing in the patient in normal use between any patient connection and all other patient connections (and not intended to produce a physiological effect)2.
Application of mains voltage on an applied part or patient lead.

## Slide 6: Patient Lead Types
IEC 60601-1 3rd edition: Medical Electrical Equipment
Patient Leads
F-Type: APPLIED PART in which the PATIENT CONNECTIONS are isolated from other parts of the ME EQUIPMENT
Type BF: F-TYPE APPLIED PART provide a higher degree of protection against electric shock than that provided by TYPE B APPLIED PARTS
Type CF: F-TYPE APPLIED PART provide a highest degree of protection against electric shock than that provided by TYPE BF APPLIED PARTS
B Type: APPLIED PART that provides protection against electric shock
Notes: F-type Applied part which is electrically isolated from Earth and other parts of the medical equipment. IE floating F-type applied part are eithr BF or CF applied part
  Type BF applied part – F type with higher degree of portection against electric shock than type B appiled parts – not suitable for cardiac applicatoins
  Type CF applied part – highest degree of portection against electrick shock – suitable for direct cardiac application
B-type
  Applied part are those parts, which are usally earth referenced
  Not suitable for direct cardiac applications

## Slide 7: How Is It Measured?
THE MAIN QUESTION TO ASK What is the severity of electric current someone would be exposed to if they were to touch the DUT under such conditions?
MD
Leakage current is measured through a human body impedance network, also known as a Measuring Device (MD)
Body Impedance
MD is designed to simulate the impedance of the human body under various conditions.
Normal and Single Fault Conditions
Measurements taken under normal conditions.
Measurements also taken under single fault conditions to simulate worst case scenarios

## Slide 8: How Is It Measured?
Medical Devices
IT Equipment
Electric Spas
MD will vary by product standard. Most MDs are derived from IEC 60990-1

## Slide 15: POLL QUESTION

## Slide 16
IEC 60601-1 Medical Equipment

## Slide 17: Patient Leakage Current

## Slide 18: Patient Leakage Current

## Slide 19: Touch Current
60601-1 – Figure 14

## Slide 20: Touch Current
60601-1 – Figure 15

## Slide 21
Touch Current

## Slide 22: Patient Auxiliary Current
60601-1 – Figure 19

## Slide 23
Patient Auxiliary Current

## Slide 24: Mains on Applied Part
60601-1 – Figure 16

## Slide 25
https://www.youtube.com/watch?v=RQcMD-5Vw3c..\Desktop\Line Leakage Testing Demonstration.mp4
Mains on Applied Parts

## Slide 26: POLL QUESTION

## Slide 27
Leakage current
Mains Voltage on Applied Part Figure 16
External voltage on SIO Figure 17
External voltage on metal accessible part that is not PE Figure 18
Additional Tests and Considerations

## Slide 28
Contact Us
If you would like a copy of this presentation please email Brittany Socha at brittany.socha@arisafety.com
Check out our website for more information arisafety.com

## Slide 29
JOIN US FOR OUR NEXT WEBINAR
Wednesday, November 15 10AM CT (GMT – 6:00) Automate Your Production Line: 6 Ways to Fully Automate Electrical Safety Testing
Click the link in chat box to learn more